## Slide 1: Virtual Moon Project
Emily Pearson
(Supervised by Andy Smith)

## Slide 2: Project Overview
Return to the moon – lunar construction
Materials in the lunar environment
Recreation of lunar conditions to assess material suitability
  Radiation – solar “cosmic rays”
  Temperature variations (>250K range)

## Slide 3
G.Heiken et al ‘The Lunar Sourcebook’ CUP (1991)
Solar radiation power
Lunar surface temperature
R.B. Malla, K.M.Brown; ActaAstronautica 107 (2015) pp.196–207

## Slide 4: Temperature Cycling
Simulation of lunar day-night cycles over shorter timescale
Heating already available
Cooling cycle – nitrogen gas flow with liquid nitrogen heat exchanger
At lunar equator: -166°C to +114°C
R.B. Malla, K.M.Brown; ActaAstronautica 107 (2015) pp.196–207

## Slide 5: Experimental Setup
Vacuum chamber with cold finger
Liquid nitrogen heat exchanger
Mass flow controller – cooling rate regulation
Solenoid valves – two gas feed lines
  One through LN2 heat exchanger
  One bypass
Arduino-based electronics
Data sent to MATLAB for processing

## Slide 6: Initial Testing – Problems Identified
Mass Flow Controller range
  Max flow rate of 1 SLPM is insufficient for cooling
  Poiseuille’s Law: assumes laminar and incompressible flow
  Flow throttling

## Slide 7: Initial Testing – Problems Identified
Nitrogen and liquid nitrogen supply
  Higher flow rate of N₂ = rapid depletion
  LN₂ boil-off rate increases with N₂ flow rate

## Slide 8: Solutions
Alternative mass flow controller
  Larger range required (ideal max. of 30 SLPM)
N₂ gas recirculation system
  Prototype under construction
Pre-cooling of N₂ gas
On site LN₂ production unit?
  Needed for long irradiations

## Slide 9: Temperature Holding
Previous tests – potential for temperature holding identified
  LN2 depleted and no N₂ flow → very slow warmup
Successfully tested:
  -40°C to -35°C range
  -60°C to -55°C range
Lower temperature ranges (e.g. lunar night) would require refills of liquid nitrogen

## Slide 11: Project Summary
Successful demonstration of liquid nitrogen heat exchanger for cooling (to min. temps of -110°C and -132 °C)
Successful demonstration of regulated cycle to hold temperature within a certain range
Identified areas for improvement
Next steps: address current limitations → enable multiple heating and cooling cycles

## Slide 12: Acknowledgements
Thank you to Andy and the accelerator team for all your help!
Thank you to everyone at DCF for welcoming me to the team this summer!

## Slide 13: Questions?